# группа: 2-СЭЗ-21

дата: 16.02.24г

урок 22  2/44

# преподаватель: Панкратова ЮВ

# обратная связь: 9061900457 Telegram

# Тема: Parts of the Building. Части здания.

Task 1. Read and translate. Прочитайте и переведите данный текст (письменно в тетрадь).

TEXT «PARTS OF THE BUILDING».

The construction of a building begins with the excavation, dug for the basement. Then the foundation walls below ground level are constructed. After this the framework is erected and clothed with various finishing materials and protected by several coats of paint.

The part upon which the stability of the structure depends is the framework. It is intended for safety carrying the loads imposed. The floors, walls, roofs, and other parts of the building must be carefully designed and proportioned.

Here are the main parts of a building and their functions. Foundations are to keep the walls and floors from contact with the soil, to guard them against the action of frost, to prevent from settlement which causes cracks in walls and uneven floors.

The more common types of foundation structures are: isolated spread footings (one to each column); combined footings (one to two columns); and mat foundations (all columns resting upon a heavy slab). These forms may sometimes rest directly on the bearing soil or they may rest on the piles. Sometimes the columns are set on large cylinder of plain concrete, from 4 to 8 ft. in diameter. This form is called «caisson» foundation.

Walls are built to enclose areas and support the weight of floors and roofs. An outside wall rests directly on the foundation wall forming a bearing unit for the upper floors and the roof inside walls serve as partitions for several rooms inside the dwelling. They may or may not support other parts of the structure. The walls may be solid and hollow. The materials used for the wall construction are brick, stone, concrete and other natural or artificial materials.

Floors divide the building into stories. They may be of timber or may be constructed of fire-resisting materials.

A roof is the topmost part of a building It covers the building and protects it from exposure to the weather. A roof must be strong enough to resist winds and support snow loads, and serve as insulations to prevent transmission of heat. Roofs tie the walls and give strength to the structure. Shapes of roofs may be flat, pitched, of domes and vaults.

Task 2. Find the definitions to the following English terms.

Подберите определения (письменно):

Framework		They divide the building into stones.

Foundations	It covers the building and protects it from exposure to the weather.

Walls	They are to keep the walls and floors from contact with the soil.

Floors	They are built to enclose areas and support the weight of floors and roofs.

Roof			The part upon which the stability of the structure depends.

Task 3. Complete the following sentences. Дополните предложения (письменно:

1) The construction of a building begins with ... 2) The framework is erected and clothed with ... 3) Framework is intended for... 4) The main parts of a building are ... 5) The more common types of foundation structure are ... 6) Foundations may rest directly on ... 7) An outside wall rests directly on ... 8) Inside walls serve as ... 9) The materials used for the wall construction can be ... 10) Floors may be of... 11) Shapes of roofs may be ...

Task 4. Answer the following questions: (письменно в тетради; 1-ый вариант- отвечает на первые 8 вопросов, 2-ой вариант отвечает на вопросы 9-16).

1) What does the construction of a building begin with?

2) What is constructed then?

3) What part does the stability of the structure depend upon?

4) What is the framework intended for?

5) What are the main parts of a building?

6) What is the function of foundations?

7) What are the more common types of foundation structure?

8) What may these forms rest on?

9) What are walls built for?

10) What wall forms a bearing unit for the upper floors and the roof?

11) What do inside walls serve as?

12) May walls be hollow?

13) What divide the building into stories?

14) What materials are used for the floor construction?

15) What is the function of roofs?

16) What shapes of roofs do you know?

Task 5. Отправить задание на электронную почту. Иметь задание в наличии в рабочей тетради.

Обратная связь: 9061900457 Telegram (если есть вопросы)

E-mail: grossbach@mail.ru отправлять задание!

P.S. если вы забыли, как читается слово, используйте Google-переводчик в своем мобильном, он проговаривает нужное слово.